## Slide 1: Computer Graphics
Textures
Teacher: Nico Pietroni
University of Technology Sydney

## Slide 2: Recap: Shape rapresentations
Points

## Slide 3: Recap: Shape rapresentations
Parametric surfaces

## Slide 4: Recap: Shape rapresentations
Implicit surfaces

## Slide 5: Recap: Shape rapresentations
Polygonal meshes

## Slide 6: Recap: Shape rapresentations
Subdivision surfaces

## Slide 7: Recap: Manifoldness
A surface is a 2‐manifold if it is everywhere locally homeomorphic to a disk.
manifold
Non-manifold
Non-manifold

## Slide 8: Recap: Orientability
A polygonal mesh is orientable, if the incident faces to every edge can be equally oriented
Notes
  An orientable surface has 2 sides
  Non manifold surfaces are non-orientable.
  Every non‐orientable closed mesh embedded in R3 intersects itself
  Manifold open mesh can be non-orientable
Klein bottle
Moebius strip

## Slide 9: Recap: Genus
The Genus of a closed surface, orientable and 2-manifold is the maximum number of cuts we can make along non intersecting closed curves without splitting the surface in two.
0
1
2

## Slide 10: Recap: Addictive FDM

## Slide 11: Texture maps! One of the most common and important asset of a game One of the most GPU RAM consumer

## Slide 12: Texture mapping
3D geometry
(set of quadrilaterals )
+
RGB texture 2D
(here: color-map)
=

## Slide 13: Example (color-map)
+
=

## Slide 14: Example (color-map)

## Slide 15: Textures in Games
The majority of visual richness perceived in the typical videogame is due to textures!
Textures resolution have more impact (quality wise) than Meshes resolution!

## Slide 16: Texture maps: data structures
Texture sheet = the image projected on the surface (the mesh)
A texel = a sample of that signal
  Between samples: (bilinear) interpolation
Texture sheet
«Texel»

## Slide 17: Textures: common terms
  Similar purpose to the per-vertex attributes!
  but…
    # texels >> # vertices
    More complex signals!

## Slide 18: The power of textures
4953 Vertices , Textured

## Slide 19: The power of textures
4953 Vertices

## Slide 20: Recap:Attribute interpolation
Attributes inside fragments are interpolated:
  from attributes at vertices
  using barycentric coordinates of the fragment as weights

## Slide 21: The power of textures
4953 Vertices , Per Vert color

## Slide 22: The power of textures
18055 Vertices

## Slide 23: The power of textures
18055 Vertices , Per Vert color

## Slide 24: The power of textures
4953 Vertices , Textured

## Slide 25: Texture maps and Meshes
Not necessarly 1:1
  1:N -- several textures «sheets» associated to a mesh
  N:1 – more meshes on the same sheet
  If different part of mesh associated to different textures: decompose the object into sub-mesh
MATERIAL
MESH B
MESH A
TEXTURE 1 BUMPMAP
TEXTURE 2 COLORMAP

## Slide 26: MIP map levels
Pre-filtering of textures
“LOD pyramid, for images”!
Hardware chooses the right level (for pixel)
Avoid subsampling artifacts
1024x1024
512x512
256x256
1x1

## Slide 27: Texture maps as assets
Carachteristics:
  Size:
    resolution
    channels (eg: alpha?)
  MIP-map
    (available of not?)
  Compression?
    e.g. quantized “color-map”, or specific compression schemes
Recurrent constraints:
Power of 2 for side
  (requested by always fewer engines)
  Both in U and V
  (e.g.: 256x256 o 1024x512)
res < max
  (e.g.: max = 4096 o 2048)

## Slide 28: Life of a Texture in a Game Engine
TextureSheet on GPU
LOAD
DISK
CENTRAL RAM
GPU RAM
Image Object
IMPORT
Image File

## Slide 29: Texture Sheets: files format
For generic images:
    .JPG / .JPEG
       lossy,
       Good compression rate
       “photographic” images: best
       only 3 channels (no choice)
       8 bit per channel (no choice)
    .PNG
       lossless
       < compression ratio
       drawings: best
       alpha channel also possible
       16bits also possible
Specialized for textures: (most used option)
    .DDS («direct draw surface») same format used in GPU. Thus:  includes MIPmap levels (if wanted)
       compression: very lossy And bad compression rate
      (and fixed)
       GPU ready! Just read from disk & load on GPU memory (no decompress / recompress!)

## Slide 30: Texture maps as assets: file formats
For generic images (decompress the entire image to access the pixels)
   compression: excellent
   loading: heavy:
    Decompress from RAM, (maybe) recompress in GPU-RAM
   MIP-map lvls etc: Controlled by the engine
For textures (random accessibility to texels, without uncompressing the entire image)
   compression: bad
   loading: light
    direct copy Disc => RAM =>GPU RAM
   MIP-map lvls etc: Controlled by the artist
asset on
disk / RAM
(maybe)
asset in GPU RAM
(for sure)

## Slide 31: Texture Sheets: in GPU RAM
Rastered images, but with peculiarity …
  mipmap levels
  channels per texels: 1,2,3, or (usually) 4
  bits per channels: usually 8, fixed point («true-color») – or compression
  resolution: powers of 2 (usually)

## Slide 32: UV-Mapping of a mesh
A mapping : mesh surface 2D texture space is needed
  «parametrization» of the surface
Idea: store this mapping as attribute: (s,t) per vertex
  The «u-v mapping» of the mesh (u,v) == (s,t)
[0..1]2

## Slide 33: Modeling task: “u-v mapping” construction
Texture “atlas” (composed of several “charts”)
u
v

## Slide 34: UV mapping: example
MESH
TEXTURE SPACE
…
u
v
N = A
A
N
B
B
C
C
(vertex seam)
M
M

## Slide 35: Texture space notation
Texture 2D
u
v
Texture Space (or “parametric space" or "u-v space")
Texture Space = [0,1] x [0,1]
eg: 512 texels
e.g.: 1024 texels
1.0
1.0

## Slide 36: Two notations
s-t (es OpenGL)
s
t
1.0
1.0
u
v
1.0
1.0
u-v
(es DirectX)
(0,0)
(0,0)
Most diffused (in game industry)

## Slide 37: Texture space independent of resolution (or shape)
Texture 2D
s
t
1.0
1.0
1024x512
s
1.0
1.0
128x64
Convenient!
We can reduce texture sheets res (balancing quality / memory) without affecting the UV mapping.
t

## Slide 38: Construction of UV-mapping: aka parametrization

## Slide 39: What is a parametrization?

## Slide 40: Parametrization for texture mapping
+
=
2D texture image
textured bunny
3D mesh
disk-like patches
texture charts
u
v

## Slide 41: Small digression: Parametrization for remeshing
f
f -1

## Slide 42: Parametrization: what we need?
A strategy to flatten a 3D surface on 2D domain
  Introducing as few distortion as possible
A strategy to introcuce cuts
3D
2D
3D
2D

## Slide 43: Cuts 1
sphere in 3D
2D surface disk
Clearly needed for closed surfaces

## Slide 44: Cuts 2
Usually more cuts -> less distortion
sphere in 3D
2D surface

## Slide 45: Cuts 3: closed surfaces
How many cuts?
for a genus 0 surface ?
any tree of cuts

## Slide 46: Cuts 3: closed surfaces
How many cuts?
for a genus 1 surface ?
two looped cuts

## Slide 47: Cuts 3: closed surfaces
How many cuts?
for a genus 3 surface ?
6 looped cuts

## Slide 48: Cuts 3: closed surfaces
How many cuts?
for a genus n surface ?
2n looped cuts
genus 6

## Slide 49: Manual Parametrization
Manual UV mapping
An advanced artistic skill

## Slide 50: What is Distortion?
Angle preservation: conformal
Area preservation: equiareal
Area and Angle: Isometric

## Slide 51: Distortion
  σ1 and σ2 describe local deformations
f
σ1
σ2
1
1
p
UV
3D

## Slide 52: Isometric Mapping
  σ1= σ2=1
  preserves areas, angles and lengths
f
1
1
1
1
UV
3D

## Slide 53: Conformal Mapping
  σ1/ σ2=1
  preserves angles
f
1
1
σ1
σ1
UV
3D

## Slide 54: Equiareal Mapping
  σ1⋅ σ2=1
  preserves areas
f
1
1
σ1
1/σ1
UV
3D

## Slide 55: Texture coordinates: Per Vertex
Compact representation
V2
V3
V5
V4
V1
T1
T2
T3
Tri: | Wedge 1: | Wedge 2: | Wedge 3:
T1 | V4 | V1 | V2
T2 | V4 | V2 | V5
T3 | V5 | V2 | V3
vert | X | Y | Z | U | V
V1 | x1 | y1 | z1 | u1 | v1
V2 | x2 | y2 | z2 | u2 | v2
V3 | x3 | y3 | z3 | u3 | v3
V4 | x4 | y4 | z4 | u4 | v4
V5 | x5 | y5 | z5 | u5 | v5

## Slide 56: Texture coordinates: Per Vertex
How to handle seams?

## Slide 57: Texture coordinates: Per Wedge
Per Wedge = per triangle per vertex
Tri: | Wedge 1: | u | v | Wedge 2: | u | v | Wedge 3: | u | v
T1 | V4 | u(T1,V4) | v(T1,V4) | V1 | u(T1,V1) | v(T1,V1) | V2 | u(T1,V2) | v(T1,V2)
T2 | V4 | u(T2,V4) | v(T2,V4) | V2 | u(T2,V2) | v(T2,V2) | V5 | u(T2,V5) | v(T2,V5)
T3 | V5 | u(T3,V5) | v(T3,V5) | V2 | u(T3,V2) | v(T3,V2) | V3 | u(T3,V3) | v(T3,V3)
vert | X | Y | Z
V1 | x1 | y1 | z1
V2 | x2 | y2 | z2
V3 | x3 | y3 | z3
V4 | x4 | y4 | z4
V5 | x5 | y5 | z5
V2
V3
V5
V4
V1
T1
T2
T3

## Slide 58: Tileable Textures
A
A
B
B

## Slide 59: Tileable textures

## Slide 60: Tileable textures
Typical use
Very efficient in space

## Slide 61: Signals typically stored in textures (in games)
Each texel a base-color (components: R-G-B)
  Texture is a “diffuse-map” / “color-map” / “RGB-map”
Each texel a transparency factor (components: α)
  Texture is an “alpha-map” o “cutout-texture”
Each texel contains a dist. From surface value
  Texture is a “bump-map” o “height-texture”
Each texel a normal (components: X-Y-Z)
  Texture is a “normal-map”

## Slide 62: Cutout textures texels = alpha (transp. lvl)
Alpha map
RGB map

## Slide 63: Cutout textures texels = alpha (transp. lvl)
  e.g.: drapes, beard...
texture

## Slide 64: Cutout textures texels = alpha (transp. lvl)
  e.g.: trees, foliage

## Slide 65: Texture mapping and Alpha Test
Eg: fur, fur coats
(repeated)
texture

## Slide 66: Bump maps or Normal Map
Bump Map
    Details encoded by storing the differences between low-res and hi-freq
    As scalars (distance along the normal)
    Used for re-tessellation, or for parallax mapping
Normal Map:
    Details encoded by storing the normals of the hi-freq surface
    Modifying the lighting

## Slide 67: Bump Map
Store the Distances of the detailed surfaces from the low-poly mesh
  example -- a bump-map for a screw-head :
Detailed surfaces (I would like to model)
head
of the screw
low-poly mesh (approximation of ^) (here: flat  )
displacement map (scalar)
0
0
0
0
.1
.5
.6
.6
.7
.5
.4
.2
0
0
0
0
0
0
0
0
0
0
0.2
0.6
0.4

## Slide 68: Bump Map
Bump Mapped
Color Only

## Slide 69: Normal Map
Store Vectors from the low-poly mesh to the detailed surfaces
Detailed Lighting (I would like to model)
low-poly mesh (here: flat  )
Normal map (vectorial)
“subsquare”! Not an height field

## Slide 70: Normal Map
+
=
Low-poly mesh (uv-mapped!)
Normal Map
lots of cheap geometric detail
(apparently)

## Slide 71: Normal Map
Same geometry (a sphere)
Different Normal-Maps

## Slide 72: Solid Textures

## Slide 73: Solid Textures
Volumetric voxellized Texture: 3D array of texels
1 texel == 1 voxel
  E.g. each voxel one color RGB  solid RGB textures
As all the textures:
  In video RAM
  Fast access during rendering
Model color onto volume
  surface + internal
  useful, e.g., for fractures
Note: no need of UV-mapping!
  Texture indexed by geometric mesh (rescaled)
Problem: ram space
  Cubic wrt the resolution

## Slide 74: Recap: Texture mapping
3D geometry
(set of quadrilaterals )
+
RGB texture 2D
(here: color-map)
=

## Slide 75: Recap: Life of a Texture in a Game Engine
TextureSheet on GPU
LOAD
DISK
CENTRAL RAM
GPU RAM
Image Object
IMPORT
Image File

## Slide 76: Recap: Parametrization for texture mapping
+
=
2D texture image
textured bunny
3D mesh
disk-like patches
texture charts
u
v

## Slide 77: Recap: Texture coordinates: Per Vertex
Compact representation
V2
V3
V5
V4
V1
T1
T2
T3
Tri: | Wedge 1: | Wedge 2: | Wedge 3:
T1 | V4 | V1 | V2
T2 | V4 | V2 | V5
T3 | V5 | V2 | V3
vert | X | Y | Z | U | V
V1 | x1 | y1 | z1 | u1 | v1
V2 | x2 | y2 | z2 | u2 | v2
V3 | x3 | y3 | z3 | u3 | v3
V4 | x4 | y4 | z4 | u4 | v4
V5 | x5 | y5 | z5 | u5 | v5

## Slide 78: Recap: Texture coordinates: Per Wedge
Per Wedge = per triangle per vertex
Tri: | Wedge 1: | u | v | Wedge 2: | u | v | Wedge 3: | u | v
T1 | V4 | u(T1,V4) | v(T1,V4) | V1 | u(T1,V1) | v(T1,V1) | V2 | u(T1,V2) | v(T1,V2)
T2 | V4 | u(T2,V4) | v(T2,V4) | V2 | u(T2,V2) | v(T2,V2) | V5 | u(T2,V5) | v(T2,V5)
T3 | V5 | u(T3,V5) | v(T3,V5) | V2 | u(T3,V2) | v(T3,V2) | V3 | u(T3,V3) | v(T3,V3)
vert | X | Y | Z
V1 | x1 | y1 | z1
V2 | x2 | y2 | z2
V3 | x3 | y3 | z3
V4 | x4 | y4 | z4
V5 | x5 | y5 | z5
V2
V3
V5
V4
V1
T1
T2
T3

## Slide 79: Recap: Tileable textures

## Slide 80: Recap:Cutout textures texels
  e.g.: drapes, beard...
texture

## Slide 81: Recap: Bump Map
Bump Mapped
Color Only

## Slide 82: Recap: Normal Map
+
=
Low-poly mesh (uv-mapped!)
Normal Map
lots of cheap geometric detail
(apparently)

## Slide 83: Computer Graphics
Textures
Teacher: Nico Pietroni
University of Technology Sydney